## Slide 1: Design of Digital Circuits Lab 4 Supplement: Finite-State Machines
Prof. Onur Mutlu
ETH Zurich
Spring 2020
20 March 2020

## Slide 2: What Will We Learn?
In Lab 4, you will implement a finite-state machine using Verilog.
Design and implement a simple circuit that emulates the blinking lights of a Ford Thunderbird.
Understand how the clock signal is derived in the FPGA board.
Write an FSM that implements the Ford Thunderbird blinking sequence.

## Slide 3: Tail Lights of a 1965 Ford Thunderbird
In this lab, you will design a finite-state machine to control the tail lights of a 1965 Ford Thunderbird.

## Slide 4: Tail Lights of a 1965 Ford Thunderbird
There are three lights on each side that operate in sequence to indicate the direction of a turn.
Copyright from ClassicLEDs.com

## Slide 5: Part 1: FSM Design
An FSM must do three things:
  Next State Logic: Determine the next state from the present state and the inputs.
  Output Logic: Determine the output signals based on the present state and input signals.
  State Register: keeps track of the present state; must be updated at every clock cycle.
  The manual contains the details of this FSM specifications.

## Slide 6: Part 1: FSM Design
An FSM must do three things:
  Next State Logic: Determine the next state from the present state and the inputs.
  Output Logic: Determine the output signals based on the present state and input signals.
  State Register: keeps track of the present state; must be updated at every clock cycle.
  The manual contains the details of this FSM specifications.
For more details please refer to lecture 6:
Slide 62: Finite-State Machines.
Slide 127: Moore vs. Mealy FSMs.

## Slide 7: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 8: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 9: Part 2: Verilog Implementation
Separate three parts of the code:

## Slide 10: Part 3: Implementing the Clock (I)
The problem of using push-buttons as clock:
  Compared to the speed of the FPGA the change in a push button is very slow (~ 1 million times slower)
  During the slow transition, the FPGA will see many fast occurring transitions and would interpret each of them as a clock edge. (Bouncing)

## Slide 11: Part 3: Implementing the Clock (II)
CLK100Mhz (W5): Your board contains a 100Mhz crystal oscillator circuit.
Problem: The clock is too fast.
Solution: A clock divider:

## Slide 12: Part 4: Defining the Constraints
We must specify constraints for:
  Buttons for control
  LEDs for output lights
  Connections for clock
The manual contains more information about the constraints.

## Slide 13: Last Words
In Lab 4, you will implement a finite-state machine using Verilog.
Design and implement a simple circuit that emulates the blinking lights of a Ford Thunderbird.
Understand how the clock signal is derived in the FPGA board.
Write an FSM that implements the Ford Thunderbird blinking sequence.
In the report you will implement a dimming function, so that the lights are not only on and off, but can have intermediate levels

## Slide 14: Report Deadline
23:59, 17 April 2020

## Slide 15: Design of Digital Circuits Lab 4 Supplement: Finite-State Machines
Prof. Onur Mutlu
ETH Zurich
Spring 2020
20 March 2020